## Slide 1: Firmware Change Notification for General SED PM893/897
2025.Oct
Samsung

## Slide 2: FW Change Notice
Affected product and Firmware version
Effective date
  Effectiveness date which team is considering : 2026. Feb(the early of Feb)
Device | P/N | FW | 
 |  | Current firmware | To Be
PM893 General | MZ7L3240HCHQ-00A07 MZ7L3480HCHQ-00A07 MZ7L3960HCJR-00A07 MZ7L31T9HBLT-00A07 MZ7L33T8HBLT-00A07 MZ7L37T6HBLA-00A07 MZ7L3240HCHQ-00B7C MZ7L3480HCHQ-00B7C MZ7L3960HCJR-00B7C MZ7L31T9HBLT-00B7C MZ7L33T8HBLT-00B7C MZ7L37T6HBLA-00B7C | JXTC604Q | JXTC904Q
PM897 General | MZ7L3480HBLT-00A07 MZ7L3960HBLT-00A07 MZ7L31T9HBNA-00A07 MZ7L33T8HBNA-00A07 | JXTE404Q | JXTE704Q

## Slide 3: 1. Guide Update related to Tempsensor failure
Problem
  SMART Trip observed if there is I2C failure or Tempsensor failure.
  HW Guide is updated in order to avoid TRIP condition.
Improvement details
  HW Guide updated for I2C Tempsensor failure case.
Severity
  Low
Likelihood
  Low
Notes: 추후 업데이트 예정

## Slide 4: 2. Assert in Fcore when multiple live dumps are collectedR
Problem
  Collecting the Live dump in a loop, which will create the same region multiple times and count reaches to MAX, which leads to device going to Error mode.
Improvement details
  Instead of adding Dump Data Range index each time Live Dump is collected , Dump Data Range is added only once when power on. This adding Dump Data Range is for adding DRAM memory to live dump excluding the L2P Range.
Severity
  High
Likelihood
  Low
Notes: 추후 업데이트 예정

## Slide 5: 3. Reclaim margin reset improvement
Enhancement
  Reclaim margin is carry forwarded across diff reclaims for the same block and not reset
Improvement details
  if a higher reclaim margin is configured for a block, the residual reclaim margin in the block if lower then current new value, will allow setting the new value.
Severity
  Low
Likelihood
  Low
Notes: 추후 업데이트 예정

## Slide 6: 4. Open fails because Debug log not saved in DTT shutdown
Problem
  UECC Observed on SMART data
Improvement details
  After DTT shutdown, Subsequent device power on sequence skip the debug log check.
Severity
  Low
Likelihood
  Low
Notes: 추후 업데이트 예정

## Slide 7: 5. Enable Conservative Sequential write check
Problem
  Measurement of long QoS 99.9% was measured and latency was captured. Other than Non-4K Ran.Wr in no other scenario significant drop is seen.
  PM883 and PM893 has different policy on Non-4K throttling , which explains that drop. This policy is there from PM883a product onwards.
Improvement details
  Enable Conservative Sequential write check and apply the delay for all sectors.
Severity
  Low
Likelihood
  Low
Notes: 추후 업데이트 예정

## Slide 8: 6. Disable Send FPDMA Command Support
Problem
  Send FPDMA Command support is Enabled
Improvement details
  Disable Send FPDMA Command support as per customer requirement
Severity
  Low
Likelihood
  Low
Notes: 추후 업데이트 예정

## Slide 9: 7. GC and EPI Policy improvement
Problem
  IO cmd Timeout
  Multiple EPI closure because of Slow host caused higher block consumption then GC. Resulting in High/Urgent GC scenario.
Improvement details
  Improved GC pace for EPI closed Blocks.
Severity
  Low
Likelihood
  Medium
Notes: 추후 업데이트 예정

## Slide 10: 8. COMRST response improvement
Problem
  Device has not responded to COMREST or sync-escape exception in less than 1sec causing drive removal from host environment.
  Improvement details
  SWI will be triggered for all the exceptions.
  If Reset is triggered while processing low exception, FW will preempt low priority exception and start processing RESET.
Severity
  Low
Likelihood
  Low
Notes: 추후 업데이트 예정